## Slide 1: UAVSAR LITE
Steven daniels
Sprint 2

## Slide 2: Sprint OBECTIVE
The goal of this sprint was to:
  Design the embedded software
  Design radar software
  Create test cases for UAVSARLITE embedded software
  Create test cases for UAVSARLITE radar software

## Slide 3: Octocopter software
STEVEN DANIELS

## Slide 4: Octocopter test cases
Define test cases for the following:
  Octocopter can be connected to a ground station via a TCP, UDP or serial connection.
  Octocopter sends (vendor, software versions, product versions information.
  Octocopter sends vehicle telemetry and state information (e.g. battery, GPS, RC connection, flight mode etc.) and set telemetry update rates.
  Octocopter performs arm, disarm, kill, takeoff, land, loiter,Waypoint, and return to launch command.
  Octocopter flys missions created by ground station
  Octocopter receives telemetry data

## Slide 5: Software dfd send flight control cmds
Pass commands to QGroundControl
(Android App)
Command Navio2 using ArduPilot
Android Device
Navio2 Flight Control Module
FC commands
FC commands
FC commands

## Slide 6: Software dfd receive flight control cmds
QGroundControl(Android App)
ArduPilot
Android Device
Navio2 Flight Control Module
FC commands
FC commands
FC commands

## Slide 7: Embedded SOFTWARE
STEVEN DANIELS

## Slide 8: Software dfd for i/q data from IWR6843AOP to UAVSARLITE_LINUX app
Store I/Q data sample using UAVSARLITE_Linux
(Raspberry Pi 4)
Send packet to UAVSARLITE_Linux
(DCA10OO
EVM)
IWR6843AOP module
RAW I/Q DATA
RAW I/Q DATA
RAW I/Q DATA
Raspberry Pi 4 GB RAM

## Slide 9: Software dfd for IMU Data from ardupilot to UAVSARLITE_LINUX app
Store MavLink data using UAVSARLITE_Linux
(Raspberry Pi 4)
Send MavLink packet to UAVSARLITE_Linux
(Raspberry Pi 3)
ArduPilot
IMU Data
Raspberry Pi 4 GB RAM
IMU Data
IMU Data

## Slide 10: Software dfd for i/q data from IWR6843AOP module to UAVSARLITE_Android app
Packet deserialization on UAVSARLITE_Android
(Android Device)
Send packet to UAVSARLITE_Android (Raspberry Pi 4)
Android Device
IWR6843AOP module
RAW I/Q DATA
Plot radar data with UAVSARLITE_Android
(Android Device)
RAW I/Q DATA
RAW I/Q DATA
RAW I/Q DATA

## Slide 11: Software dfd for IMU Data from ArduPilot (Navio2) to UAVSARLITE_Android app
Packet deserialization on UAVSARLITE_Android
(Android Device)
Send IMU data packet to UAVSARLITE_Android (Raspberry Pi 4)
Android Device
ArduPilot
(Navio2)
IMU Data
Plot radar data with UAVSARLITE_Android
(Android Device)
IMU Data
IMU Data
IMU Data

## Slide 12: Software Embedded Environment
Operating System | UBUNTU SERVER
Programming language | C++
Version Control | Git
IDE | Visual Studio
GitHub | https://github.com/level2fast/UAVSARLITE_APP
Google Drive | https://drive.google.com/drive/folders/1VCX5rsDp7lvDYmyz8F9QWnNmddW9AwOj?usp=sharing

## Slide 13: Software drone
Ground Control Station | QGroundControl | http://qgroundcontrol.com/
ArduPilot Host OS | Linux | https://ubuntu.com/download/raspberry-pi-2-3-core
Flight Control Commands protocol | MavLink | mavlink.io/en/about/implementations.html
Drone Testing | SITL | ardupilot.org/dev/docs/sitl-native-on-windows.html

## Slide 14: Control UAV
Steps to control UAV:
  Assemble Drone
  Install QGroundControl on Android Device
  Configure Navio2 Flight Control Module to use TCP connection to send data wirelessly to Raspberry Pi 4.

## Slide 15: Embedded Software Test cases
RP4_UAVSARLITE_Sender:
  Connection with Host PC
  Connection with SQLite database
  Verify UAVSARLITE data packets sent
RP4_UAVSARLITE_Receiver:
  Connection with ArduPilot
  Connection with IWR6843AOP
  Verify reception of IMU data
  Verify reception of RAW I/Q data
  Verify synchronization of IMU and RAW I/Q data
QGroundControl:
  Octocopter can be connected to a ground station via a TCP, UDP or serial connection.
  Octocopter sends (vendor, software versions, product versions information.
  Octocopter sends vehicle telemetry and state information (e.g. battery, GPS, RC connection, flight mode etc.) and set telemetry update rates.
  Octocopter performs arm, disarm, kill, takeoff, land, loiter,Waypoint, and return to launch command.
  Octocopter flys missions created by ground station
  Octocopter receives telemetry data

## Slide 16: Software embedded resources
Visual studio installation:
  https://devblogs.microsoft.com/cppblog/linux-development-with-c-in-visual-studio/
SQLite
  https://developer.android.com/training/data-storage/sqlite
  https://linoxide.com/linux-how-to/install-use-sqlite-linux/

## Slide 17: Send RADAR data to a computer wirelessly
Steps to control UAV:
  Load RTOS onto Raspberry Pi 4
    https://projects.raspberrypi.org/en/projects/raspberry-pi-setting-up/3
  Setup Visual studio development environment.
    https://marketplace.visualstudio.com/items?itemName=VisualCppDevLabs.VisualCforLinuxDevelopment
  Create c++ app that uses a wireless connection to receive data via TCP.
  Create an pc app/android app that uses a wireless connection to send data via TCP for testing.
    https://www.programminglogic.com/example-of-client-server-program-in-c-using-sockets-and-tcp/
    https://developer.android.com/training/connect-devices-wirelessly
  Send data over Wifi to PC or Android app.
    https://askubuntu.com/questions/775597/how-to-use-onboard-wifi-on-raspberry-pi-3-with-ubuntu-server-16-04
    https://hewlettpackard.github.io/wireless-tools/Tools.html
    https://stackoverflow.com/questions/45984345/how-to-turn-on-off-wifi-hotspot-programmatically-in-android-8-0-oreo

## Slide 18: Radar SOFTWARE
STEVEN DANIELS

## Slide 19: Radar sw design objectives
Define development environment
Define SAR design
  Define Radar Parameters
  Choose a SAR algorithm to implement
  Determine what IWR6843 radar configuration is best for detecting range, Doppler and creating SAR images .
  Select corner reflector design for testing radar.
  Select SAR operating mode
Create SAR I/Q data flow
Create UAVSARLITE_Data_Processor structural and block diagrams
Create SAR test cases

## Slide 20: RADAR development Environment
Operating System | Windows
Programming language | MATLAB
Version Control | Git
IDE | MATLAB
Library | Simulink Support Package for Android Devices https://www.mathworks.com/help/supportpkg/android/index.html?s_tid=CRUX_lftnav

## Slide 21: Define sar parameters
An excel spreadsheet will be used to keep track of all SAR parameters. Parameters were separated into 3 categories:
  IWR6843AOP Parameters
  "Introduction to Airborne Radar" parameters
  IWR6843AOP USRR Chirp Configuration Parameters

## Slide 22: IWR6843AOP Parameters
IWR6843AOP Parameters |  |  |  | 
Frequency |  | 60- to 64 | GHz coverage | 
Wavelength |  | 5 | mm | λ = C/f Where, λ (Lambda) = Wavelength in meters,c = Speed of Light (299,792,458 m/s),f = Frequency
Height of Antenna |  | 10.4 | mm | 
Length of Antenna |  | 10.4 | mm | 
Space between Antenna Elements |  | 2.5 | mm | 
Bandwidth |  | 4 | GHz | 4-GHz continuous bandwidth
Field Of View Azimuth |  | 130 | degrees | 130º azimuth FoV and 130º elevation FoV
Field Of View Elevation |  | 130 | degrees | 130º azimuth FoV and 130º elevation FoV
Azimuth Beamwidth(4Rx, 3Tx in Demo Visualizer) |  | 30 | degrees | https://dev.ti.com/gallery/view/mmwave/mmWave_Demo_Visualizer_IWR6843AOP/ver/1.0.0/
Elevation Beamwidth(4Rx, 3Tx in Demo Visualizer) |  | 30 | degrees | https://dev.ti.com/gallery/view/mmwave/mmWave_Demo_Visualizer_IWR6843AOP/ver/1.0.0/
Azimuth Beamwidth(4Rx, 1Tx in Demo Visualizer) |  | 60 | degrees | https://dev.ti.com/gallery/view/mmwave/mmWave_Demo_Visualizer_IWR6843AOP/ver/1.0.0/
Elevation Beamwidth(4Rx, 1Tx in Demo Visualizer) |  | 60 | degrees | https://dev.ti.com/gallery/view/mmwave/mmWave_Demo_Visualizer_IWR6843AOP/ver/1.0.0/

## Slide 23: Introduction to Airborne Radar" parameters
Introduction to Airborne Radar" parameters |  |  |  |  |  | 
2-way 4dB Beamwidth(Uniformally illuminated synthetic array) |  | 0.240385 | radians | wavelength/(2*L), where L = Length of aperture | 13.77302 | degrees
2-way 3dB Beamwidth(Uniformally illuminated synthetic array) |  | 0.211538 | radians | wavelength/(2*L), where L = Length of aperture | 12.12026 | degrees
1-way 3dB Beamwidth(Uniformally illuminated real array) |  | 0.423077 | radians | 0.88(wavelength/L), where L = Length of aperture | 24.24052 | degrees
Null to Null Beamwidth(Uniformally illuminated array) |  | 0.961538 | radians | 2*(wavelength/L), where L = Length of aperture | 55.0921 | degrees
Desired Resolution Cell Size |  |  |  | see "Introduction to Airborne Radar book" |  | 
Dimension Azimuth |  | 0.20 | ft | The distance in azimuth of the side of a resolution cell |  | 
Dimension Range |  | 0.20 | ft | The distance in range of the side of a resolution cell |  | 
Ahievable Resolution Cell Size |  |  |  | see "Introduction to Airborne Radar book" |  | 
Dr |  | N/A | ft | 500* t feet where t = compressed pusle width, required bandwidth = 1/t | N/A | 
Da |  | 61.47541 | mm | (wavelength/2L)*R where L = array length, same units as wavelength | 0.201691 | ft
Max unambiguous range(R) |  | 22500 | mm | This value is the same as USRR Chirp Configuration Parameters max unambiguous range | 73.8189 | ft
Synthetic Array Length(L) |  | 915 | mm | This value was selected to achieve a Da of .2 ft or approx 2 inches | 3.001969 | ft
Da Min(Strip map radar) |  | 5.2 | mm | Length of Real Antenna/2, ultimate resolution for a synthetic array whose beam is positioned at a fixed angle relative to the flight path, as in strip map radars Pg. 415 |  | 

## Slide 24: IWR6843AOP USRR Chirp Configuration Parameters
IWR6843AOP USRR Chirp Configuration Parameters |  |  |  | USRR = Ultra Short Range Radar, take from Texas Instruments document swra553
Max unambiguous range |  | 22.5 | m | 
Sweep bandwidth |  | 1500 | Mhz | 
Ramp slope |  | 30 | MHz/us | 
Inter-Chirp duration |  | 50 | us | 
Number of chirps |  | 128 | - | 
Range Resolution |  | 0.1 | m | c/(2*B), where c = speed of light, and B = Sweep bandwidth of FMCW chirp Calculated using matlab
Chirp Duration |  | 50 | us | 
Max unambiguous relative velocity |  | 35.5 | kmph | 
Max beat frequency |  | 4.5 | MHz | 
ADC sampling rate (complex) |  | 5 | Msps | 
Number samples per chirp |  | 250 |  | 
Range FFT size |  | 256 | - | 
Frame time (total) |  | 12.8 | ms | 
Frame time (active) |  | 6.4 | ms | 
Radar data memory required |  | 512 | KB | For 1 radar data cube

## Slide 25: Radar dfd i/q data
MMWAVEIC
BOOST
IWR6843AOP module
Android Device
RF Data
RAW I/Q DATA
DCA10OO
EVM
Raspberry
Pi 4
RAW I/Q DATA
RAW I/Q DATA
RAW I/Q DATA
RAW I/Q DATA

## Slide 26: Corner reflector
A radar corner reflector is used to test the SAR. Radar corner reflectors are designed to reflect the microwave radio waves emitted by radar sets back toward the radar antenna. This causes them to show a strong "return" on radar screens.
To recognize the shapes of objects on the ground such as vehicles, houses, and small buildings a fine resolution is required. As a rule, the required resolution distance is somewhere between 1/5th and 1/20th of the major dimension of the smallest object to be recognized.

## Slide 27: corner reflector
Five Oceans Radar Reflectors, 12" x 12"

## Slide 28: Sar image
  SAR-mode “Stripmap”
    The conventional SAR strip mapping mode assumes a fixed pointing direction of the radar antenna broadside to the platform track. A strip map is an image formed in width by the swath of the SAR and follows the length contour of the flight line of the platform itself. A detailed description of this mode you'll find on the topic SLAR.

## Slide 29: Uavsarlite_Data_processor

## Slide 30: Uavsarlite_data_processor

## Slide 31: Radar Software Test cases
UAVSARLITE_Data_Processor
  Verify linear FM chirp signal
  Verify range compressed signal
  Verify Doppler centroid frequency
  Verify Range Cell Migration Correction interpolator
  Verify Azimuth reference signal
  Verify Azimuth compressed signal
  Verify Single Look Complex image for target

## Slide 32: Radar Simulation in Matlab EXAMPLES
Build Radar Cube:
  https://www.mathworks.com/company/newsletters/articles/building-and-processing-a-radar-data-cube.html
Phased Array System Toolbox:
  https://www.mathworks.com/help/phased/index.html?s_tid=CRUX_lftnav
FMCW Antenna Sim:
  https://www.mathworks.com/help/phased/examples/patch-antenna-array-for-fmcw-radar.html
Phased Array Design and Analysis:
  https://www.mathworks.com/help/phased/phased-arrays.html?s_tid=CRUX_lftnav
Array Pattern Synthesis:
  https://www.mathworks.com/help/phased/examples/array-pattern-synthesis.html

## Slide 33: RADAR resources
SAR Training by NASA
  https://www.asf.alaska.edu/data-tools/sar-training-processor/
Matlab
  https://www.mathworks.com/help/supportpkg/android/index.html?s_tid=CRUX_lftnav
  https://www.mathworks.com/help/pdf_doc/supportpkg/android/index.html
https://www.radartutorial.eu/01.basics/!rb02.en.html
https://ocw.mit.edu/resources/res-ll-003-build-a-small-radar-system-capable-of-sensing-range-doppler-and-synthetic-aperture-radar-imaging-january-iap-2011/projects/

## Slide 34: Radar resources continued
Google drive
http://dev.ti.com/tirex/explore/node?node=ANHO2DdQ523mY5JJ5JzDdg__VLyFKFf__LATEST
http://dev.ti.com/tirex/explore/node?node=AJcVbr8AiXNoaBv.wihv2w__VLyFKFf__LATEST
http://dev.ti.com/tirex/explore/node?node=ANyYfhPgBXNj1C.iwjUscA__coGQ502__LATEST
Introduction to Airborne Radar by George W. Stimson
Digital Processing of Synthetic Aperture Radar Data by Ian Cummings and Frank Wong
http://dev.ti.com/tirex/explore/node?node=ANyYfhPgBXNj1C.iwjUscA__coGQ502__LATEST